## Slide 1
TEAM CYGNUS
TATA TECHNOLOGIES INNOVENT 2026
AeroSentinel
Edge-Native Intelligence for Aerospace MRO
Offline, Real-Time Aircraft Surface Defect Detection
Medi-Caps University, Indore
B.Tech Computer Science — Pre-Final Year
Category: Edge AI | Aerospace MRO
Notes: Introduce the team and project. Emphasize: fully offline, runs on a laptop, no cloud needed.

## Slide 2
The Problem
02
Human Inspection Failures
Manual visual inspection is still the industry standard. Inspector fatigue, inconsistent hangar lighting, and subjective judgment lead to missed defects. Aviation safety bodies consistently cite human error during MRO as a top contributor to aircraft incidents.
Cloud Dependency in the Field
AI-assisted inspection tools route imagery to centralized cloud servers. In remote hangars, forward operating bases, and island airports — where MRO is most critical — bandwidth is limited or absent. Latency stretches from seconds to hours, grounding aircraft when every minute counts.
The Gap: No reliable, offline-capable AI system exists for real-time MRO defect detection independent of network infrastructure.
Notes: Two compounding problems: fatigue-driven human error + cloud latency. The gap is the combination of both.

## Slide 3
Objective & Approach
03
Objective: Build a fully offline, software-defined computer vision pipeline that detects aircraft surface defects in real-time on standard CPU hardware — with zero cloud or network dependency at any stage.
Edge-First Design
Inference runs entirely on a local CPU using ONNX Runtime. No cloud calls at any stage.
Optimized Model
YOLOv8n fine-tuned on industrial defect data, exported to INT8 ONNX via Static PTQ for <30ms latency.
Explainability
Grad-CAM overlays show technicians exactly what drove each detection — not just a bounding box.
Full Workflow
From image capture to offline PDF maintenance report, the complete MRO workflow runs air-gapped.
Notes: Four pillars: edge-first, optimized model, explainability, full MRO workflow. All four are necessary together.

## Slide 4
Solution Overview — System Architecture
04
Camera
Capture
OpenCV
Preprocessing
CLAHE + Resize
ONNX Inference
YOLOv8n INT8
Post-Processing
NMS + Severity
Dashboard
& Report
Streamlit + PDF
Grad-CAM (On-Demand)
PyTorch .pt — Explainability Layer
100% Air-Gapped
Zero bytes leave the device. Sensitive MRO data never crosses a network.
<30ms Per Frame
Static INT8 PTQ locks activation ranges. Real-time on any i5-class CPU.
Dual-Model Design
ONNX for speed. PyTorch retained on-demand for Grad-CAM explainability.
Notes: Walk through the pipeline left to right. Emphasize the Grad-CAM branch is on-demand (ONNX incompatibility). Mention the three callouts at the bottom match the core claims.

## Slide 5
Solution Deep Dive — Dashboard & Reporting
05
Streamlit Dashboard (Local Browser)
Upload Image
Live Camera
Confidence
Severity Filter
Export PDF
[Annotated Aircraft Frame]
CRITICAL
92%
MEDIUM
78%
Defect Log
Time
Class
Conf
Severity
14:32:01
Corrosion
92%
CRITICAL
14:32:04
Crack
78%
MEDIUM
Live Annotated Feed
Bounding boxes with class labels, confidence and severity tier drawn per frame.
Severity Heatmap
Aggregated spatial risk map overlaid on aircraft silhouette.
Timestamped Defect Log
Sortable table: class, confidence, severity, bounding box coordinates.
Offline PDF Report
fpdf2 report: aircraft ID, date, annotated images, sign-off block. Zero network calls.
Notes: Show the dashboard mockup. Key: everything runs in the browser locally. PDF export happens offline. No network calls at any stage.

## Slide 6
Challenges Faced
06
CRITICAL
NEU Dataset Domain Gap
Challenge:
NEU dataset is flat steel imagery. Aircraft surfaces are curved, painted, and lit differently in hangars.
Mitigation:
Heavy Albumentations augmentation: perspective warps, CLAHE contrast shifts, synthetic crack overlays, hangar lighting simulation — applied before training.
CRITICAL
Grad-CAM / ONNX Incompatibility
Challenge:
Grad-CAM requires PyTorch autograd graph. ONNX Runtime decouples the model from PyTorch — Grad-CAM cannot run on ONNX models.
Mitigation:
Dual-model architecture: ONNX Runtime for primary inference. PyTorch .pt model retained separately, loaded on-demand for explainability, then unloaded to free RAM.
MODERATE
INT8 Quantization Accuracy Drop
Challenge:
Static PTQ can degrade small-object detection (hairline cracks, small fasteners) — the exact defects that matter most.
Mitigation:
Per-channel quantization (vs per-tensor). Decision matrix: drop <2% → ship; drop 2–4% → per-channel retry; drop >4% → escalate to QAT.
MODERATE
Heuristic Severity Triage
Challenge:
No learned severity classifier exists for this PoC scope. Rule-based triage on detection area × confidence is not aerospace-grade.
Mitigation:
Documented explicitly as a PoC-scope simplification. Production path: trained classifier head validated against ASME/SAE defect grading standards.
Notes: Be ready to explain the Grad-CAM/ONNX incompatibility in detail — this is the question most technically sophisticated judges will ask.

## Slide 7
Technical Implementation
07
Training
PyTorch + Ultralytics YOLOv8
Google Colab T4 GPU. Transfer learning. 100 epochs, batch 16, img 640.
Augmentation
Albumentations
Perspective warp, CLAHE, brightness, synthetic crack overlay.
Export
ONNX
Framework-agnostic model format. Dynamic axes for flexible input.
Quantization
ONNX Runtime PTQ (INT8)
Static PTQ with CalibrationDataReader on 100 augmented images. Per-channel.
Inference
ONNX Runtime (CPU Provider)
<30ms per frame. No GPU. InferenceSession + NMS post-processing.
Vision
OpenCV
Resize 640×640, normalize, CLAHE on grayscale channel.
Explainability
pytorch-grad-cam
On-demand. Last conv layer hook. Heatmap overlaid on source frame.
Dashboard
Streamlit
Local browser UI. st.cache_resource for model warmup.
Reports
fpdf2
Offline PDF. Header, annotated images, defect table, sign-off block.
Notes: Nine layers, each with a specific role. Judges will likely probe: why ONNX over TFLite, why static PTQ over dynamic, why Streamlit over custom UI.

## Slide 8
Results & Impact
08
<30ms
Inference per frame
on CPU hardware
85%+
mAP@0.5 target
on test set
~75%
Model size reduction
FP32 → INT8
30-45%
Aircraft downtime
reduction (projected)
Diagnostic Latency Comparison
Chart: Minutes
| Cloud Pipeline (remote hangar) | AeroSentinel (Edge)
Latency | 180 | 0.03
Hours → Seconds
2-6hr cloud lag compressed to <30ms at the point of inspection.
$10K-$150K/hr Saved
Reducing MRO turnaround directly cuts costly aircraft downtime.
Fatigue Error Eliminated
AI maintains consistent >85% mAP regardless of shift length.
Zero Data Exposure
All structural data stays on the local edge device. Air-gapped.
Notes: The chart is the money shot — 180 minutes vs 0.03 minutes. Let it land. Then walk through the four impact bullets.

## Slide 9
Demonstration
09
PoC Demo Video
90-second screen recording
(To be embedded / linked in Drive folder)
Demo Script
1
Show network adapter disabled
2
Launch Streamlit dashboard (local)
3
Upload sample defect image
4
Inference: <30ms, bounding boxes + severity
5
Walk defect log table
6
Toggle Grad-CAM heatmap overlay
7
Show severity heatmap
8
Export offline PDF report
9
Confirm: network still disabled
Notes: This slide holds the video. Step 1 (network disabled) is the most important — it proves the offline claim before you even show detection.

## Slide 10
Future Enhancements
10
OpenVINO Optimization
Export to Intel OpenVINO INT8 for x86 CPUs. Projected 40-50% further latency reduction over ONNX Runtime on Intel hardware.
Quantization-Aware Training
If Static PTQ accuracy drop exceeds threshold, retrain with simulated INT8 precision using QAT — forces the model to adapt to quantization during learning.
Real Aerospace Dataset
Supplement NEU with actual aerospace inspection imagery (fuselage, nacelle, wing surfaces) to fully close the domain gap from flat steel to curved aircraft surfaces.
Learned Severity Classifier
Replace heuristic area×confidence triage with a trained classifier head, validated against ASME/SAE defect grading standards for production-grade severity scoring.
Fleet-Level Aggregation
Extend to multi-aircraft defect tracking across a fleet. Detect systemic structural patterns across registration IDs over time.
Hardware Security Module
Integrate HSM-based authentication for report signing, ensuring tamper-proof maintenance records acceptable to airworthiness regulators.
Notes: First two (OpenVINO + QAT) are near-term technical iterations. Real aerospace dataset is the biggest accuracy unlock. Learned severity classifier is the production readiness gate.

## Slide 11
Project Plan — 14-Day PoC Roadmap
11
Phase 1
Days 1–4
Data & Training
Acquire NEU dataset
Run augment_offline()
Fine-tune YOLOv8n/s
Evaluate ≥90% mAP baseline
Phase 2
Days 5–6
Edge Optimization
Export to ONNX
Static PTQ with CalibrationDataReader
Validate INT8 mAP drop <2%
Benchmark <30ms on CPU
Phase 3
Days 7–9
Vision Pipeline
OpenCV preprocessing module
ONNX Runtime InferenceSession
Heuristic severity triage
Grad-CAM on-demand integration
Phase 4
Days 10–12
Dashboard & Reports
Streamlit local dashboard
Severity heatmap overlay
Timestamped defect log
fpdf2 offline PDF report
Phase 5
Days 13–15
Testing & Demo
End-to-end offline validation
Cross-platform (Win + Linux)
requirements.txt + setup script
90-second demo recording
InnoVent Timeline
Registration
Deadline
5 July 2026
PoC Build
Complete
~July 2026
Virtual POC
Presentation
October 2026
Final
Demo Day
January 2027
Notes: Judges want to see this is achievable. 14 days is realistic with the structured phases. The InnoVent timeline shows Virtual POC is October — that's the real build deadline, not the form submission.

## Slide 12
AeroSentinel
Edge-Native Intelligence for Aerospace MRO
Team Cygnus | Medi-Caps University, Indore | Tata Technologies InnoVent 2026
Offline. Real-Time. Explainable.
No cloud. No latency. No missed defects.
Notes: Closing slide. Reiterate the three-word tagline. Thank judges and open for Q&A.